## Slide 1: PowerPoint 1: Materials science principles
PowerPoint presentation
2. Construction science principles
2.1 Materials science principles

## Slide 2: Materials: an introduction
PowerPoint presentation
A wide range of materials are used in buildings. The choice of material depends on its properties and intended use. Properties of materials include their durability, weather resistance, heat resistance, water resistance, conductivity and malleability.
The principles of materials science help to ensure buildings perform well over time: that they are durable and stable.

## Slide 3: Examples of different materials
Ferrous and nonferrous metals
Plastics (thermosetting and thermoplastic)
Fireclays/ceramics
Bricks
Concrete
Mortar
Plasterboard
Timber
Fibre-based sheet
Paint
Solvents
Adhesives
Sand
Lime
Additives

## Slide 4: Metals
Iron and mild steel are ferrous metals. Steel is used for structural applications such as portal frames. Magnetic effects only work with ferrous metals.
Non-ferrous metals are more resistant to corrosion than ferrous metals. They include aluminium, copper and lead.
Copper is a pure metal that is used for water and heating pipework as it doesn’t react with water, ensuring the water remains uncontaminated.

## Slide 5: Plastics
Thermosetting plastics become rigid when heated and do not soften when reheated. For example, epoxy resins used in anchor bolts.
Thermoplastic is a flexible plastic that becomes pliable and solidifies. It can be recycled. Good examples are guttering and downpipes and electrical insulation on cables.
Cross-linked polyethylene (XLPE) is a form of polyethylene with cross-links. It is used in building services pipework systems, hydronic radiant heating and cooling systems, domestic water piping and insulation for high tension (high voltage) electrical cables. Compared to thermoplastic polyethylene, XLPE does not melt and is thermally resistant, as well as being more resistant to environmental stress.

## Slide 6: Ceramics and fireclays
Ceramics –toilet pans and cisterns are made from ceramics which are coated with a slip which is fired to form an impervious layer. Ceramics are also used on isolators in electrical systems, such as an electric rail line.
Fireclays are a refractory material that is resistant to decomposition by heat, pressure or chemical attack, and retains strength and form at high temperatures. Fire bricks are used for lining furnaces and fireplaces.

## Slide 7: Types of brick
When used as a material for constructing cavity walls, brick can broadly be split into two categories:
Face brick can used for the external finish of a structure. There are a huge range of face bricks in many different colours and textures that allow the architect to design a building that will look good for many years to come.
face brick
common brick.
Common brick will usually be covered by some form of render or cladding. It can be manufactured from clay or concrete.

## Slide 8: Engineering brick
Engineering brick is a dense brick manufactured from clay which becomes vitreous when fired in a kiln. This means that it has low water absorption levels, making it less prone to frost damage.
This type of brick can is suitable for exposed positions in a structure and provides effective weathering features such as projecting sills at door and window openings.
Engineering brick can also be used as a damp proof course (DPC)
in a cavity wall. This is not often the case since these types of brick are expensive. A minimum of two courses is required to prevent rising damp in an outer leaf of brick masonry.

## Slide 9: Blocks
Blocks can be manufactured from coarse aggregate or thermal insulation materials such as pulverised fuel ash (PFA).
Coarse aggregate blocks are usually referred to as concrete blocks. They can be made as a dense block or lightweight block depending on the type of aggregate used.
Dense concrete blocks can be used in situations where there is a need for the masonry to resist compressive forces, such as in a cavity wall footing below ground or in a load-bearing wall above ground.
Lightweight concrete blocks can be used in situations such as non load-bearing partition walls.

## Slide 10: Thermal insulation blocks
Thermal insulation blocks are made from cement, lime, sand, pulverised fuel ash (PFA) and water.
PFA is mixed with sand and water to form a slurry. This is then heated before being mixed with cement, lime and a small amount of aluminium sulphate powder.
The aluminium reacts with the lime to form bubbles of hydrogen. These tiny bubbles or voids act as a barrier to reduce heat transfer.
A more recent material used to manufacture thermal insulation blocks is hemp.
Notes: Find out more about brick here Guides - The Brick Development Association

## Slide 11: Technical information data sheets
Technical information data sheets from manufacturers provide information about the qualities of bricks including:
classification
size
compressive strength
water absorption
durability
soluble salt content.
Fir examples, see: Abbey Blend Brick Datasheet.pdf (forterra.co.uk)

## Slide 12: Mortar
Mortar is mixed according to specified ratios.
The ideal ratio is the same whether the mortar is mixed by hand or by machine.
The mortar mix ratio will be specified according to the masonry material being used.
The ratio of the mix should produce a mortar that is slightly less hard than the bricks or blocks being laid.
This allows for any slight movement in the masonry caused by thermal expansion or by shrinkage during hardening.

## Slide 13: Mortar ratios
A ratio of 1:5 represents a mortar mix containing one part of cement to five parts of sand.
To make it stronger, we would reduce the amount of sand. Reducing the proportion of sand to three parts would give us a stronger mortar mix of 1:3
Bricks and blocks vary in hardness and compressive strength. The mortar mix required will depend on the brick materials used.

## Slide 14: More on mix ratios
A dense concrete block manufactured from coarse aggregate will require a harder mortar mix ratio than a lightweight thermal insulation block manufactured from pulverised fuel ash. The mix ratio for thermal insulation blocks will be weaker to allow for thermal movement.
If the mortar mix ratio for thermal insulation blocks is too strong, cracking will occur at window and door openings and at junction walls.
Softer materials such as calcium silicate bricks (sometimes referred to as sand/lime bricks) or softer types of clay bricks require a weaker mortar mix ratio.

## Slide 15: Mixing methods
Mortar is increasingly mixed by automated mechanical methods which means that the specified ratio is produced more reliably. In addition, consistency of workability and colour is easier to achieve.
adequate compressive strength
durability – resistance to chemical attack and frost damage
strong bonding with masonry components
a sealed surface to protect against wind-driven rain.
Whatever method is used to produce mortar, the specified mix ratio must be adhered to in order to achieve:

## Slide 16: Concrete technology

## Slide 17: Cement
Concrete relies upon cement as the active ingredient that binds all the other ingredients together. Cement reacts by hardening, using a process of hydration in which the bonds are formed over time.
Concrete has to be cured to allow it to attain sufficient strength so its formwork can be removed.
Curing is important and may require some or all of the following:
spraying the surface of the concrete with a curing membrane to retain the water
covering the concrete with insulation blankets in cold weather
spraying the concrete with water.

## Slide 18: Classifications of concrete
The UK classifications of concrete are as follows. Each is designed to specify the use of concrete according to its final function.
Standard prescribed mixes ST1, ST2, ST3, ST4, ST5.
General concrete GEN0, GEN1, GEN2, GEN3.
Reinforced concrete RC20/25, RC23/30, etc.
Paving concrete PAV1, PAV2.
Foundation concrete FND2, FND3, FND4.

## Slide 19: Research tool
You will find the Hanson website very useful for learning more about concrete. It helps to answer many common questions, such as why foundation concrete has a unique specification (to resist sulphate attack within contaminated soils), which additive is used in paving concrete (an air entrainment additive), and where you would use GEN0 concrete (in non-structural applications).
https://www.hanson.co.uk/en/ready-mixed-concrete/technical-information/types-of-concrete

## Slide 20: Concrete tests
Notes: Tutor to explain how a slump test is conducted

## Slide 21: Slump test

## Slide 22: Strength test
The cube is then tested under a compression load and the results noted at 7, 14, 21 and 28 days.
Cubes are made using a 25mm square tamp bar.
They are trowelled smooth and allowed to cure.

## Slide 23: Timber
Timber falls into two main categories: hardwood and softwood.
The names imply that these materials are either hard or soft, but this is not necessarily the case. The terms hardwood and softwood refer to the type of tree that the timber has been cut from. Hardwoods are deciduous trees, softwoods are coniferous trees.
Examples of softwood | Examples of hardwood
European redwood | Oak
Whitewood | Ash
Douglas fir | Beech

## Slide 24: Timber types
The two types of tree have different types of timber and a different type of structure to that timber.
Softwoods such as whitewood are generally used for carcassing (studwork, joists and rafters), while high-quality structural work and joinery use redwood and Douglas fir.
Hardwoods tend to be used for heavy structural work and fine-quality joinery.
Whitewood
Oak

## Slide 25: Manufactured boards
Timber can be processed into manufactured board. The most common are:
MDF (medium-density fibreboard)
chipboard
OSB (orientated strand board)
plywood
hardboard
blockboard.
Plywood is made from many thin layers (or laminates) stuck together at right angles to each other, making it strong.

## Slide 26: Plasterboard
Plasterboard is a rectangular sheet manufactured from a gypsum core, sandwiched between lining paper on both sides.
It is used as a background surface in new and traditional buildings to form a dry construction background known as ‘dry lining’.
It is a pre-made dry product that only requires ﬁnishing by applying a setting coat. Edges are either tapered or square.
Plasterboard can be standard or performance rated. Performance plasterboard is designed to meet specific requirements and is colour-coded (sound insulation, fire resistance, insulation, moisture resistance).

## Slide 27: Paint
There are two basic types of paint: water-borne and solvent-borne.
Water-borne coatings are those where the binder is dispersed in the water – the water then evaporates as the coating dries.
Solvent-borne coatings are those where the binder is dissolved in a solvent – the solvent also evaporates as the coating dries.

## Slide 28: Components of paint
Pigments/dyes: the solid particle ingredients that provide colour, opacity or ‘hiding power’, adhesion and, in some cases, the main form of protection.
Film former/binder: binds the other ingredients together and forms the protective film that adheres to the substrate.
Solvent: used to dissolve the binder into liquid form – it evaporates during the drying process.
Thinner: liquid that is most often added on site to reduce the viscosity of a coating to help application. This also evaporates during drying.
Extender: a ‘cheaper’ form of pigment used to bulk up and provide body for a coating. Its use will often reduce quality and price.
Other additives can be used to give the paint different characteristics or qualities – such as texture in the case of masonry paints – or fire resistance.

## Slide 29: Types of surface coating
Different paint coatings are suitable for different uses depending on their finish and durability.
Primers/sealers: for wood, metal, plaster, plastics etc.
Undercoats: intermediate coatings applied before finishes.
Finishing paints: gloss, eggshell, satin, emulsion, masonry.
Interior paints: for interior surfaces only.
Exterior paints: for exterior surfaces only (eg masonry paint).
Stains/varnishes: for bare or previously painted wood.
Preservatives: used on exterior woodwork.

## Slide 30: Properties of materials
Chemical composition – a term that is often used to define the composition of soils. For example, alkaline soil, where sulphate-resistant cement would have to be specified.
Ductility – the ability of a material to be drawn out under tension without breaking. Gold is an example of a ductile material.
Malleability – the ability of a material to be hammered or rolled into a shape. For example, cold-formed sheeting.
Conductivity – the ability of a material to allow an electrical charge to pass through and along it. Copper wire is highly conductive.

## Slide 31: Properties of materials
Tensile strength – the resistance of a material to being torn apart. For example, a tie in a cavity wall has tensile strength.
Compressive strength – the strength of a material to resist force and weight directly applied to it. For example, a foundation has compressive strength.
Strength – the measure of tensile, shear and compressive forces on a material and its ability to withstand such forces, stresses and strains.
Durability – the useful life of a product in terms of years. For example, brick, stone and steel all have high durability.

## Slide 32: Failure and degradation
Time, ultraviolet (UV) light and weathering from the elements all contribute to the degradation of a material, for example:
a clay brick will absorb water which freezes in winter and expands, causing damage to the face of the brick
timber, if untreated, will absorb water and fungus and deteriorate by rotting
sunlight discolours some plastic materials (eg roof lights) causing them to become brittle and crack.

## Slide 33: Environmental conditions
Oxidation of metals – aluminum, if unprotected, will oxidise in the atmosphere, creating a coating on the surface.
Rust – iron is widely used in building construction and it is important to protect it from rust. Metals such as aluminium, chromium and zinc are higher than iron in what is called the electromotive series (see Slide 35). This means that although they corrode more readily, they produce oxides that form a thin coating which then protects them from further deterioration.

## Slide 34: Environmental conditions
Atmospheric corrosion – acid rain is a primary source of corrosion, caused by sulphur dioxide from burning fossil fuels.
UV and heat damage to plastics – frequent hot summer days can cause plastics to weaken and bend.
Electrolytic corrosion is caused by the action of water. Dissimilar metals (eg copper and aluminium) in the presence of an electrolyte (water) generate an electrical charge which causes corrosion.

## Slide 35: The electromotive series and erosion
In the electromotive series, metals are ordered by their tendency to be oxidised, ie how reactive they are. Lithium is easily oxidised whereas gold is not and is therefore not reactive. This quality can be important for choosing materials which do not corrode easily (eg copper piping).
Finally, the mechanical movement of parts causes a form of corrosion known as erosion corrosion. You may know this as ‘wear and tear’. As moving parts operate, they become worn. Destroying or weakening something gradually in this way is another definition of corrosion.

## Slide 36
Any questions?