## Slide 1: PowerPoint 3: Design principles (1)
PowerPoint ation
3. Construction design principles
3.2 Design principles

## Slide 2: Introduction
In this presentation, we will examine some of the factors that need to be considered during the design of building services and how the range of design principles are influenced by the end design.
environmental protection: sustainable technologies and materials, energy sources, energy reduction materials, local and natural environment
safety: safe construction methods

## Slide 3: Sustainability
Over the last few decades, the world has developed a throw-away culture. These days, we are very aware of the impact this has had on the environment, including how fossil fuel use causes pollution and damage to wildlife habitats.
Within the developed countries, new and existing development has a responsibility to reduce waste, protect natural resources, reduce our carbon footprint and release greenhouse gases. Renewable energy sources and improved insulation are helping to reduce energy use, the life cycle of a building and waste by reducing:
use of fossil fuels and the carbon, CO2 and toxic waste produced from burning them
damage caused to the natural environment from extracting fossil fuels from the ground and impact on plants/animals within the affected ecosystems.

## Slide 4: Environmental protection
Many factors need to be considered during the design stage of any construction or building services project. Environmental protection encompasses more than the physical impact of the structure on the local environment; there are holistic effects, too. For example, what sustainable technologies and materials are proposed? Are they coming from a sustainable source? Can they be recycled? What is the carbon footprint?
Sustainable technologies: newly developed composite materials such as Ferrock and Timbercrete can replace concrete. Technologies such as BIM, and recycling heat, smart glass, cool roofs plus many other innovations all have a part to play in environmental protection.
Sustainable materials: bamboo, cork, wood, sheep's wool, straw bales and recycled steel/plastics all provide alternatives to unsustainable materials.

## Slide 5: Heat loss

## Slide 6: Insulation and energy conservation
By insulating lofts, brick cavities and ground floors (with slab or roll insulation), windows and doors (with double or triple glazing, K glass and draught excluders), energy use is significantly reduced, saving natural resources and money.
.

## Slide 7: Renewable/sustainable energy sources – solar thermal
Solar thermal (hot water) systems use free heat from the sun to warm domestic hot water. These systems include a conventional boiler auxiliary heat source to top up the hot water temperature.

## Slide 8: Renewable /sustainable energy sources – solar PV
Solar photovoltaic (PV): solar panels work by absorbing sunlight with photovoltaic cells.
The cells generate direct current electricity that is converted to alternating current to be used in the home.

## Slide 9: Renewable/sustainable energy sources – wind turbines
Micro-wind: wind turbines work by taking the energy from the wind, which turns the turbines blades connected to a generator that produces electricity.

## Slide 10: Renewable/sustainable energy sources – hydroelectric
Micro-hydro: a hydro turbine works in a similar way to a wind turbine, except the energy is taken from moving water rather than wind.

## Slide 11: Renewable/sustainable energy sources – air source heat pumps
Air source heat pumps: these work by absorbing heat from the air in a fluid and running it through a compressor. This increases the temperature of the water, which can be used to heat the home or as hot water.

## Slide 12: Renewable/sustainable energy sources: ground source heat pumps
Ground source heat pumps: these work the same as air source heat pumps, except the heat is taken from pipes sunk into the ground.

## Slide 13: Renewable/sustainable energy sources – tidal
Wave and tidal energy can generate electricity from the movement of wave and tidal flows. Turbines placed on the surface of the ocean in tidal areas generate electricity when the tide ebbs and flows. The power that results can be harnessed and supplied to the grid.
Notes: https://lh3.googleusercontent.com/proxy/nf4I1_2tlNXiFykgTnmYWahM9FcwK4NTS54lXnC9VEtAbIY0GqnC3rFiCfIM80zB_9UTSHbyX8ohtHm-7cYpI7s5LeZo6to

## Slide 14: Energy reduction
The carbon footprint of a building can be reduced by using locally sourced materials, which are not transported over long distances and which compliment any existing properties in the area.
Energy and natural resource reduction can also be achieved through: checking use on a smart meter; improving insulation to reduce heat loss; positioning windows/openings to maximise on natural light and reduce heat loss; air filtration/recirculating systems.

## Slide 15: Water conservation
Most modern appliances are water efficient by design. But water use can be reduced in several other ways, too.
A modern flush is water efficient.
Grey water harvesting includes rainwater collected and stored to flush toilets (it doesn’t have to be drinking quality).
It also includes clean water used for washing and food preparation, then used to top up harvested water or as irrigation watering for the garden.

## Slide 16: Safe construction methods
Historically, construction has a reputation of having a dangerous working environment.
To mitigate as many hazards and risks as possible, safe working practices are implemented.
Chart: Causes of construction accident (%) Source: HSE, Nov 2020
| Falls from height | Trapped by something collapsing/overturning | Struck by moving/falling object | Struck by vehicle | Contact with electricity
 | 47 | 16 | 12 | 10 | 4
Safe working practices should be considered when the build is designed, to ensure the site can be safe accessed and the project can be safely delivered. For example, can roofs be constructed off site, to reduce the number of people working at height?
Notes: Source: https://www.roofingtoday.co.uk/wp-content/uploads/2020/11/HSE-annual-Stats-2019-20-construction-pub-4-11-20-2.jpg

## Slide 17: E.R.I.C. – what it means
Eliminate: can you eliminate the risk? – e.g. construct a roof at ground level then crane on to the wallplate; replace a harmful material (e.g. asbestos) with one that is safer to work with (e.g. cellulose fibres) for insulation.
Reduce: can you reduce the risk? – e.g. by doing high-risk tasks at a time when fewer people are on site? Can you replace noisy equipment with quieter models, or limit the time people are exposed to high levels of noise?
Isolate: can the risks be isolated? – e.g. by spraying in a sealed booth; using guarding on machines to prevent physical contact.
Control: can the risk be controlled? – e.g. by using safety systems such as CO monitors; by having bespoke training in place; by planning and organising a work system that includes risk assessments and method statements.

## Slide 18: Points to remember
Accident: event causing injury or damage that could have been avoided if correct procedures were followed. Accidents NEVER just happen, they are caused.
Hazard: anything that could cause damage or harm (e.g. water on the floor).
Risk: the chance, probability or outcome of any hazard (e.g. slipping on a wet surface).
Risk assessment: identifies the hazard and risk factors that have the potential to cause harm; analyses the level of risk; lists control measures to eliminate or control the hazard.
Method statement: details exactly how to carry out a task safely. Also known as ‘Safe System of Work’, these are used alongside risk assessments.

## Slide 19: Construction (Design and Management) Regulations 2015
The CDM Regulations are intended to ensure that health and safety issues are properly considered during a project’s development so that the risk of harm to those who build, use and maintain structures is reduced. The aim of the legislation is to ensure that:
Work is planned so the risks involved are managed from start to finish
Everyone involved has the right information about the risks and how they are being managed
Construction teams cooperate and coordinate their work and communicate effectively
Workers are consulted about the risks and how they are being managed
Notes: For more see:
CDM 2015 - Designing Buildings Wiki
The Construction (Design and Management) Regulations 2015 (legislation.gov.uk)

## Slide 20
Any questions?