## Slide 1: PowerPoint 4: Design principles (2)
PowerPoint
3. Construction design principles
3.2 Design principles

## Slide 2: Design principles – factors to consider
There are many factors to consider during the design of buildings:
aesthetics
buildability
construction methods
inclusivity and accessibility
regulations
restrictions
planning requirements.

## Slide 3: Design principles – infrastructure considerations
Design principles for national infrastructure set out four key considerations.
Climate: infrastructure must help set the trajectory for the UK to achieve net zero greenhouse gas emissions by 2050 or sooner and be capable of adapting to climate change.
People: projects should be human scale, instinctive to use, and seek opportunities to improve the quality of life for people who live/work nearby.
Places: schemes should provide a sense of identity for communities, supporting the natural and built environment, and enriching ecosystems.
Value: should be added beyond the main purpose of the infrastructure, solving problems well and achieving multiple benefits.

## Slide 4: Aesthetics
These are the many factors that can affect the design of a building or structure.
Colour: use of various materials and shades – e.g. block, stone, glass, UPVC cladding, steel
Shape: the patterns or lines of brick work, cladding, glass, steel framework
Texture: materials have different textures, from rough cut stone to polished concrete, rough sawn or dressed timber, textured and smooth paint finishes
Location: can affect choice of materials selected to blend into the environment
Planning: local authorities may stipulate the materials used as part of the planning agreements

## Slide 5: Buildability
Buildability can best be defined as the ability to build. A design might work on paper but not in real life.
Buildability is the extent to which the design of a building facilitates ease of construction subject to the overall requirements for the completed building, making for a quick cost-effective and productive outcome.
Notes: See the link below to an American video on buildability for learners to watch: https://youtu.be/fXSjeVYOKSY

## Slide 6: Traditional construction methods
Despite advances in construction technologies, the demand for housing and the need to improve current building practices, many building companies are still sticking to what is best described as traditional, tried-and-tested construction methods, e.g.:
on-site brick and block external wall construction
in situ roof erection
traditional plastering
working from architects’ drawings
using sub-contractors to carry out specific tasks.

## Slide 7: Traditional methods – advantages and disadvantages
Advantages | Disadvantages
It is how many tradespeople were trained | Increased wastage of materials
Doesn’t require additional set up fees | Missed deadlines due to inclement weather
No expensive up-front investments | Missed deadlines due to lack of personnel at key times

## Slide 8: Modern construction methods
Prefabricated flat pack systems: wall and floor panels are fabricated off-site in a workshop ready to be joined on-site. They can include services, windows, doors and decorative finishes.
Thin joint masonry: uses a 3mm bed of mortar, which cures faster than the traditional 10mm. The blocks are twice the size of traditional blocks, allowing for a greater area to be constructed in less time.
Precast foundations: cast in a factory to the client’s specification and fitted to piles on site. They require less excavation and are not as weather dependent allowing for greater productivity.

## Slide 9: Traditional versus modern methods – roofing
Site carpentry working at height for the full duration of the task
Roof constructed at ground level and lifted on to structure; limited time working at height

## Slide 10: Blockwork
Traditional blockwork requires 10mm of mortar, which takes time to cure – resulting in fewer courses being laid in a day
Modern thin joint system dries quicker; no pointing required so more courses can be laid in a day

## Slide 11: Plastering verses dry lining
Traditional plastering uses large quantities of water and takes time to dry out; still extensively used; lime-based plasters will be specified for heritage work
In dry lining, plaster boards are dot and dabbed to a wall, and the joints are taped and jointed; very little water is used so the moisture content of the building is vastly reduced, along with dry times
Notes: https://image.shutterstock.com/image-photo/construction-under-building-mason-plastering-260nw-1351923029.jpghttps://northeasttapingandjointing.co.uk/wp-content/uploads/2016/01/NETJ2-300x225.jpg

## Slide 12: Prefabricated modular construction
Fabricated in a factory away from its final location, a modular construction is cost effective because it is built in a controlled environment normally using sustainable materials with improved thermal and acoustic levels of insulation.
All doors, windows and services can be pre-fitted, reducing waste because the working environment is constant.
Often designed using BIM – services etc. are planned into the design from the outset.
Work can be carried out year round.
Issues are addressed prior to site delivery.

## Slide 13: Timber-framed construction
This is not a new method of building; it has been used for centuries. However, with modern materials, insulation and working practices, timber-framed properties have become a more sustainable alternative to brick-built homes. They have better thermal performance than masonry, with a thinner wall thickness.
Example of a timber-framed construction

## Slide 14: Structural insulated panels (SIPs)
SIPs are fabricated in a factory environment, sharing the same benefits as modular construction.
SIPs arrive on site as a flat pack. They are fitted together to form the main structure, then fitted out with services once the structure is watertight.

## Slide 15: RIBA – Royal Institute of British Architects
The Royal Institute of British Architects (RIBA) have created a Plan of Work designed to offer a comprehensive framework for successfully organizing a building project. The Plan organizes the process of briefing, designing, construction and operating building projects into eight stages:
Stage 0 – Strategic definition
Stage 1 – Preparation and briefing
Stage 2 – Concept design
Stage 3 – Spatial co-ordination
Stage 4 – Technical design
Stage 5 – Manufacturing and construction
Stage 6 – Handover
Stage 7 – Use
Notes: Detailed tasks aligned to the RIBA Sustainable Outcomes Guide – GHA Knowledge Base (goodhomes.org.uk)

## Slide 16: RIBA Plan of Work
At each of the eight stages, the Plan of Work defines the:
Stage outcome (i.e. what will be achieved by the end of the stage)
Core tasks during the stage
Core statutory process (i.e. planning, building regulations and health and safety)
Procurement route (i.e. confirming the client teams involved at each of the project stages)
Information exchanges at the end of the stage (i.e. who needs to know what information and how it is communicated)
Notes: For more see: RIBA Plan of Work (architecture.com)

## Slide 17: Building Regulations – what they cover and protect
All new builds and adaptions to existing buildings must meet the current Building Regulations. These comprise several approved documents, each covering a specific area.
The Building Regulations are intended to protect the end users’ safety, health and welfare in and around buildings. The regulations are also designed to improve the conservation of fuel and power, protect and enhance the environment, and promote sustainable development.

## Slide 18: Building Regulations approved documents
Approved Document | Document Title
Part A | Structural safety
Part B | Fire Safety
Part C | Resistance to contaminant and moisture
Part D | Toxic substances
Part E | Resistance to the passage of sound
Part F | Ventilation
Part G | Sanitation, hot water safety and water efficiency
Part H | Drainage and waste disposal
Part J | Heat producing appliances
Part K | Protection from falling, collision and impact
Part L | Conservation of fuel and power
Part M | Access to and use of buildings
Part N | Glazing safety
Part P | Electrical safety
Part Q | Security
Part R | Physical infrastructure for high speed electronic communications networks
Approved document 7 | Workmanship and material

## Slide 19: Accessibility and inclusivity
Approved Document M outlines ease of access to, and use of, buildings – including facilities for disabled visitors or occupants, and the ability to move easily through a building easily (e.g. to toilets and bathrooms).
It also outlines guidance on the use of ramps and steps for ease of access, plus information on safe degrees of pitch and dimensions when building wheelchair-accessible facilities. The construction of accessible stairs and corridors is also addressed, including the safe height of stairs, and the accessible width of both corridors and stairs.
An accessible, spacious bathroom with wider doorways to enable easy access for disabled occupants.

## Slide 20: Heritage buildings
This is any building of historical and cultural importance to the community. These are often listed buildings.
Grade 1: buildings of exceptional interest, of the highest significance.
Grade 2: buildings of special interest, warranting every effort to preserve them.
Grade 2*: particularly important buildings of more than special interest.
Legislation covering listed buildings and conservation areas includes the Listed Building and Conservation Areas Act 1990.
Breaches to legislation or damage caused can lead to a fine and/or a court order stipulating that all work is undone, and the building returned to its original state.
Notes: https://www.legislation.gov.uk/ukpga/1990/9/contents

## Slide 21: Working on a heritage or listed buildings
Listed building consent is needed before work can begin on any listed building. This consent is in addition to any planning regulations that normally apply.
Permission can only be granted by the local planning authority or the Secretary of State.
The Royal Crescent, Bath is a Grade I Listed building
Notes: Full details can be found following link below.
https://ecab.planningportal.co.uk/uploads/1app/guidance/guidance_note-listed_building_consent.pdf https://www.legislation.gov.uk/ukpga/1990/9/contents

## Slide 22: Local authority restrictions
A style of house or design feature that might be acceptable in one area might not be acceptable in another – even within the same local authority’s boundaries.
Local planning authority restrictions would ensure that the houses above would be unlikely to be built next door to each other. Why do you think this is the case?

## Slide 23
Any questions?