## Slide 1: PowerPoint 5: Roles of different disciplines involved in the design process
3. Construction design principles
3.3 Roles of different disciplines involved in design

## Slide 2: What architects do
Architects liaise with clients to determine their full requirements, and prepare concept drawings and models. Once the design has been agreed with the client, they produce drawings and specifications along with relevant construction documentation.
Architects lead and develop projects from an initial concept through the whole design process.
They work with civil and structural engineers, ensuring all technical issues in the design stage are addressed.

## Slide 3: What planners do
Planners are responsible for ensuring projects stay track by producing reports and using project management tools to ensure other teams involved are on target. They:
create, maintain and review a programme of work
ensure projects are completed on time and within budget
liaise with surveyors, engineers and architects
break down large jobs into phases of development
use project management tools to plan timeframes
work with estimators to calculate the resources needed for a project
plan contingency programmes in case timeframes change.

## Slide 4: What structural and civil engineers do
Civil engineers tend to work on infrastructure projects such as bridges, roads, railways, airports, dams, power plants, sewage systems, mains water, gas and electrical services.
Structural engineers tend to specialise in the design and physical integrity of a structure ensuring the safety of that structure throughout its lifespan. They calculate weight and loads imposed, enabling architects to include these within their drawings.

## Slide 5: What land surveyors do
Land surveyors measure and map the topography of the land. The rest of the design team uses this information to plan the locations of buildings, roads position and runs for services, etc.
During the construction process, the surveyor sets out from a given datum point all levels, locations and so on.
Notes: http://gridmarksurvey.com/wp-content/uploads/2019/07/teeside-43-aspect-ratio-16x11-e1568917918831.jpg?x53058

## Slide 6: What quantity surveyors do
Quantity surveyors have wide-ranging roles including: carrying out feasibility studies, and calculating the quantities of all materials, labour and time required to complete the project (including project costings).
They also prepare tender and contractual documents (bill of quantities), negotiate contracts to main and sub-contractors, and monitor the construction process, performing risk management and cost-controlling measures.

## Slide 7: What building inspectors/building control officers do
foundations before concrete is poured
substructure up to the damp proof course
superstructure before roof
insulation levels
air flow tests
a final check before signing off where they check over the whole project.
These inspectors/officers ensure the building (or extension to an existing building) meets the minimum standards of safety, sustainability and accessibility as set out in the Building Regulations. They are appointed by the client or local authority, and visit a construction project at set times to check that all building regulations are being adhered to. Examples of checks carried out include:

## Slide 8: Example of a building inspector’s checklist
Notes: https://wpz.sungaiminify.pw/img/6f6e3bea33fd0c4863e1326c7537f82e.jpg

## Slide 9: What a draftsperson does
The draftsperson works directly with construction staff, sales staff and customers to produce drawings from written and verbal requirements. They read customers’ technical requirements and transpose them to designs that are fit for purpose. Using 2D/3D CAD modelling tools, they create original designs and modify/improve existing designs including the correct selection of materials.
Tasks include:
providing technical support
using corporate drawing standards as guidelines
gaining approval of all drawings
maintaining a drawings database.

## Slide 10: What CAD technicians do
Traditionally known as a draftsperson, they use CAD software to produce working drawings and plans used in both the building service and construction sectors. They liaise with architects and designers to produce 2D and 3D models.
Notes: https://damassets.autodesk.net/content/dam/autodesk/www/solutions/cad-software/mechanical-engineers-thumb-600x300.jpg

## Slide 11: What BIM designers do
BIM designers use various tools and technologies to produce intelligent 3D models used to integrate building services into the fabric of the building. Information can be pulled from the model and used for costings, producing bills of quanties, and aid in running and maintaining a building through its life cycle.
.

## Slide 12: What the Clerk Of Works (COW) does
The COW oversees work quality on behalf of the architect or client depending on contract size. They check that plans/specifications produced by the design team have been met. Other duties include:
reviewing designs/drawings at an early stage
highlighting potential buildability/design issues
monitoring the installation, testing and commissioning of building services
identifying defects during construction and at handover
keeping detailed records of work progress and issues that effect it.

## Slide 13: Trade occupations for onsite construction
Bricklayer: uses bricks and blocks to construct interior and external wall
Carpenter/joiner: positions and fixes timber materials and components
(first fix – installs floor joists, boards and stud partitions, and roof trusses and timbers; second fix – installs doors, kitchen units, architraves and skirting boards)
Painter/decorator: applies paints, wall coverings and other materials to finish a room; sometimes helps clients with interior design
Plasterer: applies plaster to interior walls so decoration can be applied; renders exterior walls

## Slide 14: Trade occupations for building services
Electrician: designs, installs and maintains electrical systems including wiring, sockets and lights Gas engineer: designs, installs and maintains gas appliances and pipe work systems Heating engineer: designs, installs and maintains heating appliances, radiators, controls and pipe work systems
Plumber: designs, installs and maintains sanitary appliances, and hot, cold, central heating and rainwater pipe work systems and components Protection systems engineer: designs, installs and maintains CCTV, fire alarms and automatic door controls Refrigeration and air conditioning engineer: designs, installs and maintains cooling systems in buildings

## Slide 15: The role of manufacturers and suppliers
Before designing a bespoke or a large project, it is advisable to discuss with manufacturers and suppliers what new materials, technical updates or inventions are available. What lead times are required? Will the new products reduce construction and/or maintenance costs, improve the aesthetics or improve energy efficiency?
For example, insulated concrete is a quick and energy efficient method of construction saving up to 60% on long term energy usage and improved R value of 58%.

## Slide 16: Construction project team hierarchy ‒ example 1

## Slide 17: Construction project team hierarchy ‒ example 2

## Slide 18: Your progression routes through the industry
As you start your training for a trade and develop new skills, be aware that opportunities may arise for to progress. What you study now will give you the necessary underpinning knowledge and practical experience to take advantages of these opportunities. All that’s required is hard work and the desire and commitment to achieve your goals.
Notes: For more see: www.housebuildingcareers.org.uk
For interactive models of careers in construction see: Explore a modern home building site | Housebuilding Careers

## Slide 19
Any questions?